## Slide 1: Projet: SmartGarden

## Slide 2
Le projet consiste à construire et mettre en œuvre plusieurs stations météo autonomes pour analyser l'évolution des trois jardins intérieurs du bâtiment de télécom paris. On dispose des capteurs hygro/température, d'abri, de batterie, de panneaux solaires.
Notre objectif est d’ assembler et programmer les stations
Presentation

## Slide 3
1
CD Système

## Slide 4: Cahier des Charges
Le système doit calculer la fréquence des variations de température par deux capteurs SHTC3 et SHT20 , détecter les hautes fréquences et comparer les capteurs entre eux.
Le système doit être connectée à une batterie et mesurer la tension de la batterie.
et essayer de charger la batterie a l’aide du panneau solaire.
Le firmware pourra être écrit avec l'environnement de développement ESP-IDF et les valeurs mesurées doivent être transmises en WiFi ou par port série puis stockés pour permettre l'analyse.

## Slide 5
2
Composants

## Slide 6: Liste des Composants : Carte Electronique
SparkFun ESP32 Thing:
18 analog-to-digital converter (ADC) channels
3 SPI interfaces
3 UART interfaces
Two I2C interfaces
16 PWM outputs
2 digital-to-analog converters (DAC)
Two I2S interfaces

## Slide 7: Liste des Composants : Capteurs de température
 | Capteur de température et d'humidité SHT20 I2C (sonde étanche) -Interface I2C -température: - 40 °C à 125 °C - humidité: 0 à 100 %RH - Précision: ± 3 %RH et ± 0,5 °C Temps de démarrage: 8 ms
 | Capteur de température et d'humidité SHTC30 I2C -Interface I2C -température: - 40 °C à 125 °C - humidité: 0 à 100 %RH -Précision: ± 2 %RH et ± 0,2 °C Temps de démarrage: 1 ms

## Slide 8: Liste des Composants : Panneau PV
XTPower® SP7BL 6.5 W Solar Backpack:
6.5 watt solar cells
USB output 5V 1A
dimensions: 52 cm x 22 cm

## Slide 9
3
Synoptique

## Slide 10: Synoptique du système
ESP32
SHT 20
SHTC3
PV
Diviseur de tension
I2C
I2C
Analog
Routeur
WIFI
Domain+server
Requetes HTTP

## Slide 11: Wi-Fi Initialization and Event Handling
wifi_event_handler
Handling events like connection, disconnection, and IP acquisition
Provides feedback through printf statements
Initialization phases:
  TCP/IP initiation (esp_netif_init)
  Event loop creation (esp_event_loop_create_default)
  WiFi station creation (esp_netif_create_default_wifi_sta)
  WiFi initialization (esp_wifi_init)
WiFi configuration setup and connection.

## Slide 12: HTTP Server Setup
Configuration setup using httpd_config_t
Default configuration using HTTPD_DEFAULT_CONFIG
Setting server port and address for the local server:
config.server_port = 80;
config.server_addr.sin_addr.s_addr = inet_addr("192.168.2.1");

## Slide 13: HTTP URI Handlers and Structures
URI handler functions for GET and POST requests
get_handler for HTTP GET requests
post_handler for HTTP POST requests
Definition of URI handler structures:
httpd_uri_t uri_get for GET requests
httpd_uri_t uri_post for POST requests

## Slide 14: Starting and Stoping the Web Server
Generating default configuration
Starting the HTTP server with httpd_start and Registering URI handlers
Stopping the HTTP server with httpd_stop

## Slide 15: The Main Function
nvs_flash_init for Non-Volatile Storage
Calling wifi_connection and start_webserver
Initializing and configuring ESP32 for Wi-Fi and HTTP server

## Slide 16: ESP32 configuration
We use the ESP-IDF Configuration Menu (idf.py menuconfig) for a more interactive way to set these configurations.
Wi-Fi Configuration
#define CONFIG_WIFI_SSID "your_wifi_ssid"
#define CONFIG_WIFI_PASSWORD "your_wifi_password"
#define CONFIG_WIFI_MODE WIFI_MODE_STA
Serial Communication Configuration
#define CONFIG_ESP_CONSOLE_UART_BAUDRATE 115200
Memory Configuration
#define CONFIG_ESPTOOLPY_FLASHSIZE "4MB"
#define CONFIG_ESP32_ENABLE_PSRAM
CPU Frequency
#define CONFIG_ESP32_DEFAULT_CPU_FREQ_160